## Slide 1: BioSEAL: In-Memory Biological Sequence Alignment Accelerator for Large-Scale Genomic Data
Department of Electrical Engineering
Technion
Roman Kaplan, Leonid Yavits and Ran Ginosar

## Slide 2: Part 1: Background and Previous Work
Motivation
Background:
  Content Addressable Memory (CAM)
  Associative Processing
  Memristors
Previous work: Resistive CAM (ReCAM)

## Slide 3: Motivation: Overcome the von Neumann Bottleneck
Traditional processing: Mem ↔ CPU / GPU
Major bottleneck for big data workloads
Even worse in a datacenter
11000101…
Micron’s Hybrid Memory Cube

## Slide 4: Background: Content Addressable Memory
Large array of bitcells (usually #Rows #Columns)
Search in parallel for a specific pattern
Rows
Columns
Bit
Bit

## Slide 5: Content Addressable Memory (CAM)
Compare
Compare Pattern
(1X01…0)
Matching
Rows
1
0
1
0
0
1
0
1
X
X

## Slide 6: Content Addressable Memory (CAM)
Matching
Rows
0
1
0
1
CAM Bitcell
CAM Bitcell
CAM Bitcell
CAM Bitcell
1
0
CAM Bitcell
CAM Bitcell
Write
Write Pattern
(0X10X…X)

## Slide 7: Associative Processing
Also called “Lookup table” computing
Uses compare-write combinations
  Goes over the entire truth-table
Trades time for (much) less logic
  E.g., half-adder requires 4 compare-write combinations (8 cycles)
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 8: Toy Example: Associative Vector Addition
2 |  | 0 | 2 |  | 0 | 2 |  | 0 | 
0 | 1 | 0 | 1 | 1 | 0 |  |  |  | 
1 | 0 | 1 | 0 | 1 | 0 |  |  |  | 
1 | 1 | 0 | 1 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 1 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 | 1 | 0 |  |  |  | 
0 | 1 | 0 | 1 | 0 | 1 |  |  |  | 
1 | 0 | 1 | 1 | 1 | 0 |  |  |  | 
1 | 1 | 1 | 0 | 0 | 1 |  |  |  | 
Memory map
A
B
S
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A0+B0 Cout , S
Cout
Half Adder Truth table

## Slide 9: Example: Associative Vector Addition
2 |  | 0 | 2 |  | 0 | 3 |  |  | 0
0 | 1 | 0 | 1 | 1 | 0 |  |  |  | 
1 | 0 | 1 | 0 | 1 | 0 |  |  |  | 
1 | 1 | 0 | 1 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 1 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 | 1 | 0 |  |  |  | 
0 | 1 | 0 | 1 | 0 | 1 |  |  |  | 
1 | 0 | 1 | 1 | 1 | 0 |  |  |  | 
1 | 1 | 1 | 0 | 0 | 1 |  |  |  | 
Memory map
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Half Adder Truth table
0
0
0
0
Compare
Write
0
1
0
1
0
1
0
1
0
1
0
1
A
B
S
Cout
Evaluation

## Slide 10: Example: Associative Vector Addition
Memory map
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0
Full Adder Truth table
2 |  | 0 | 2 |  | 0 | 3 |  |  | 0
0 | 1 | 0 | 1 | 1 | 0 |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 |  |  |  | 1
1 | 1 | 0 | 1 | 0 | 1 |  |  |  | 1
0 | 0 | 1 | 1 | 1 | 1 |  |  |  | 0
1 | 1 | 0 | 0 | 1 | 0 |  |  |  | 0
0 | 1 | 0 | 1 | 0 | 1 |  |  |  | 1
1 | 0 | 1 | 1 | 1 | 0 |  |  |  | 1
1 | 1 | 1 | 0 | 0 | 1 |  |  |  | 0
Compare
Write
1 | 0
0 | 1
0 | 1
1 | 0
1 | 0
0 | 1
0 | 1
1 | 0
0
0
0
1
0
0
0
1
A
B
S
Cout

## Slide 11: Associative Processing – Main Takeaway
2 |  | 0 | 2 |  | 0 | 3 |  |  | 0
0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
A
B
S
Vector length
does not matter
Processing in a fixed number of cycles, regardless of dataset size

## Slide 12: So What’s New? Memristors
Devices that change resistance with applied voltage
Non volatile
Can be placed in metal layers
above silicon
Small area footprint: 4F2

## Slide 13: Resistive CAM Bitcell
CAM bitcell: 10 transistors  2 transistors + 2 memristors
CMOS CAM bitcell (10T)
Resistive CAM bitcell (2T2R)
Kaplan, R., Yavits, L., Ginosar, R. and Weiser. “A Resistive CAM Processing-in-Storage Architecture
for DNA Sequence Alignment.” IEEE Micro, 37(4), pp.20-28, 2017.

## Slide 14: ReCAM Crossbar – Single Chip
Rows
(16M)
Data row: 256bit
2T2R Bitcell
(ReRAM)
Logic next to data
CAM registers
TAG
1-bit TAG connection (shift down)
Kaplan, R., Yavits, L., Ginosar, R. and Weiser. “A Resistive CAM Processing-in-Storage Architecture for DNA Sequence Alignment.” IEEE Micro, 37(4), pp.20-28, 2017.

## Slide 15: Compare in ReCAM
Kaplan, R., Yavits, L., Ginosar, R. and Weiser. “A Resistive CAM Processing-in-Storage Architecture for DNA Sequence Alignment.” IEEE Micro, 37(4), pp.20-28, 2017.
All rows are precharged
Mismatching rows cause a discharge through low-resistance memristor
0
1
1
0
1
0
0
1

## Slide 16: ReCAM Operations
Two instruction types:
  In-row (e.g., A+BC)
  Shift-down by one row
Multiplication is implemented as a combination of ‘+’
Cycles per operation:
32 bit | 
Instruction | Cycles
B  A + B | 256
C  A + B | 512
Row-wise Max (A, B) | 64
Max Scalar (A) | 128
Shift down by one row | 128

## Slide 17: Part 2: Our Contribution, BioSEAL
ReCAM drawbacks & our solutions
New ReCAM: Batch Write ReCAM (BW-ReCAM)
BioSEAL Array
Performance and energy efficiency comparsions to other architectures

## Slide 18: ReCAM Drawback #1
In each data row, most compare operations mismatch
  Every truth table entry matches only one row
Solution: NAND, instead of NOR
Match: discharge
Mismatch: no discharge
NAND CAM Bitcell
Precharge

## Slide 19: NAND ReCAM
Circuit simulation (32 bitcells)
1
1
2
2

## Slide 20: ReCAM Drawback #2
The same output value is written in separate cycles
Solution
Improved TAG logic: Batch-writes to one cycle
Input |  |  | Output | 
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Batch
Writes
Input |  |  | Output | 
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
16 cycles
(One write cycle per entry)
12 cycles
(One write cycle per output value)
1 Write
cycle
1 Write
cycle

## Slide 21: Batch-Write TAG
Performance Improvement over non-BW
Full adder: 25% less cycles
Logic operations: 25-37.5% less cycles
Why useful in Bioinformatics?
Amino acid scoring matrix (e.g., BLOSUM)
Full matrix is 23x23  529 truth table entries
1058 cycles to cover the entire matrix with old TAG
 544 cycles with BW (48.5% less)

## Slide 22: BW-ReCAM
Circuit & Logic
28nm SPICE simulations for timing and functionality
Logic synthesized for 28nm node process
NOR vs NAND Array (28nm)
Bitcells are 2T2R  No area differences
NAND: reduces energy by 26% on arithmetic ops
  Possible with several optimizations
Non-BW vs BW TAG (28nm)
Area: +13% for BW TAG (=40% of row area)
Energy: up to +3% due to larger BW TAG circuit
  TAG circuit = 5% of chip energy
BW-ReCAM (28nm)
For die area: (4Gb)
At 500MHz, dissipates 220W (arithmetic and logic operations)

## Slide 23: BioSEAL Array
All BW-ReCAM chips are daisy chained
  TAG of each chip connected to the chip below
  Virtually forming a long memory
Microcontroller: (1) issues instructions
(2) maps variables to bit columns
BW-ReCAM Chip
BW-ReCAM Array

## Slide 24: Local Sequence Alignment on BioSEAL
Finds similarity between two sequences (DNA/protein)
Also called Smith-Waterman algorithm (S-W)
Requires to calculate a dynamic programming matrix
  Time complexity:
Previous work1 showed S-W implementation in PRINS
[1] R. Kaplan, L. Yavits and R. Ginosar. "A Resistive CAM Processing-in-Storage Architecture for DNA Sequence Alignment."
IEEE Micro 37.4 (2017): 20-28.
Dynamic Programming Matrix
BW-ReCAM Memory
Map
a
a

## Slide 25: Multi Smith-Waterman on BioSEAL
New algorithm to align an entire database with a query
Exploits Flags (bits) and associative processing “tricks”
Each pairwise alignment has its max score
  Found by a max score reduction step
  Adds 17% per-iteration overhead, mitigated
  by the parallelism
BW-ReCAM Memory Map
Separate pairwise alignments
(performed in parallel)

## Slide 26: Performance and Energy Efficiency Comparison
Compared with large-scale systems
Performance: measured in Cell Updates per Second (CUPS)
Energy efficiency: measured in CUPS per Watt
Chart: Performance (TCUPS)
| SWAPHI-LS | RIVIYERA | CUDAlign 4.0 | PRINS | Swhybrid
Other work | 0.111 | 6 | 11.1 | 27 | 1.05
BioPRINS | 6.1 | 26.6 | 24.2 | 31.8 | 6.9
Chart: Energy Efficiency (TCUPS/Watt)
| SWAPHI-LS | RIVIYERA | CUDAlign 4.0 | PRINS | Swhybrid
Energy efficiency | 0.14 | 7.7 | 0.1 | 11.8 | 1.6
BioPRINS Energy eff. | 15.6 | 15.3 | 15.6 | 15.8 | 15.9
Other works vs BioSEAL
[1] Liu, Y., et al.. SWAPHI-LS: Smith-Waterman Algorithm on Xeon Phi coprocessors for Long DNA Sequences. CLUSTER 2014. June (2014), 257–265.
[2] Wienbrandt, L. The FPGA-Based High-Performance Computer RIVYERA for Applications in Bioinformatics. (2014), 383–392.
[3] Sandes, E.F. de O. et al.. CUDAlign 4.0: Incremental Speculative Traceback for Exact Chromosome-Wide Alignment in GPU Clusters. IEEE TPDPS. 27, 10 (Oct. 2016).
[4] R. Kaplan et al. A Resistive CAM Processing-in-Storage Architecture for DNA Sequence Alignment. IEEE Micro 37.4 (2017): 20-28.
[5] Lan, H.et al. SWhybrid : A Hybrid-Parallel Framework for Large-Scale Protein Sequence Database Search. IPDPS 2017, pp. 42-51.
[1]
[2]
[3]
[4]
[5]
[1]
[2]
[3]
[4]
[5]
384 GPUs  12 BW-ReCAM chips

## Slide 27: Thank you